`	Bat Detector Kit Instructions

Date:	18/10/16	Version:	1.0	By:	Matt Little

Build your own Bat Detector! / Bats use ultra-sonic pulses to navigate and to detect prey. These pulses are very high pitch (around 5 times the maximum frequency humans can hear). / This electronic circuit converts the high pitched sounds produced by bats to a human-audiable level. / It has a sensitivity control to adjust for different conditions. / It can also be used to listen to other high frequencies such as peeling sticky tape, compact fluorescent lights and power supplies. / This kit, although easy to build, requires quite a lot of soldering so will take in the region of 2-3 hours.

Parts included:
			Ultrasonic receiver		LED	5.1V Zener

								2 x 1N4148 / Diodes
								Speaker

								PP3 battery clip
13 x Resistors								16 x Capacitors

								Potentiometer

								Transistor

		PCB		Switch	3 x IC holders	3 x ICs

Enclosure Parts:
Front		4 x spacers
Back
2mm end		6 x M3 Hex / Spacers

4 x 3mm wide cut-out end
3mm end		6 x M3 12mm / machine screws
		6 x M3 6mm machine screws

Parts list:
Item	Ref	Item	Ref
PP3 Battery Clip	BT1	47k Resistor	R1, R2
100uf Capacitor	C1, C2, C15	10 ohm Resistor	R3
220nf Capacitor	C3	1.3k Resistor	R4
47nf Capacitor	C4, C6	150k Resistor	R5
220uf Capacitor	C5	100k Resistor	R6
2.2nf Capacitor	C7	1k Resistor	R7,R8,R14
1.5nf Capacitor	C8	470k Resistor	R9
100pf Capacitor	C9, C16	560k Resistor	R10
1nf Capacitor	C10	100 ohm Resistor	R11
33nf Capacitor	C11	10k Resistor	R12
470pf Capacitor	C12,C13	20k Potentiometer	RV1
100nf Capacitor	C14	40mm Loudspeaker	SP1
5.1V Zener Diode	D1	Switch	SW1
1N4148 small signal Diode	D2,D3	LM386 Audio Amplifier IC	U1
5mm Red LED	D4	TL074A Quad-comparator IC	U2
Ultrasonic Receiver	P1	4024 Counter IC	U3
BC337 Transistor	Q1
Enclosure
Front	x1	3mm PCB spacer rings	x4
Back	x1	M3 Hex spacers 9mm	x6
2mm Clear Spacer	x1	M3 6mm machine screws	x6
3mm Wide Spacer (marked "M")	x4	M3 10mm machine screws	x6
3mm narrow spacer	x1

Tools required:

PCB Instructions:
Step: 1	Solder resistors
		Value Ref Colour / 47k R1, R2 Yellow, Violet, Orange, Gold / 10 R3 Brown, Black, Black, Gold / 1.3k R4 Brown, Orange, Red, Gold / (This resistor is blue) / 150k R5 Brown, Green, Yellow, Gold / 100k R6 Brown, Black, Yellow, Gold / 1k R7,R8,R14 Brown, Black, Red, Gold / 470k R9 Yellow, Violet, Yellow, gold / 560k R10 Green, Blue, Yellow, Gold / 100 R11 Brown, Black, Brown, Gold / 10k R12 Brown, Black, Orange, Gold / Insert and solder the resistors. / Polarity does not matter for resistors. / Ensure they are soldered flat close to the PCB. / Use a multimeter or colour code chart to ensure correct resistor values.

Step: 2	Solder capacitors
First solder the non-polarised capacitors. / Orientation of these does not matter: / Value Ref Marking / 220nf C3 .22K63 (cream box) / 47nf C4, C6 47nK100 (cream box) / 2.2nf C7 2n2K100 (cream box) / 1.5nf C8 152 (brown blob) / 100pf C9, C16 101 (brown disk) / 1nf C10 1nK100 (cream box) / 33nf C11 33nK100 (cream box) / 470pf C12,C13 471 (brown disk) / 100nf C14 .1K63 (cream box) / Next solder the polarised capacitors. Ensure correct orientation of these components. / The negative lead is marked with a white strip. The positive lead is slightly longer than the negative. Align the positive lead with the + sign and the negative lead with the white PCB marking. / Value Ref Marking / 100uf Capacitor C1, C2, C15 10V 100uf / 220uf Capacitor C5 16V 220uf

Step: 3	Solder diodes
		There are 4 diodes to solder. / Ensure correct orientation for these components. / First solder the LED into D4. / The long lead is positive, so place that into the hole marked +. The negative side is slightly flat. / Then solder the 5.1V zener diode into D1. This diode is on its own and has very tiny marking of “5V1”. Ensure the black band aligns with the white band marked on the PCB. / The solder the remaining 2 diodes into D2 and D3. These have tiny markings saying “4148”. Ensure the black band aligns with the white band marked on the PCB.

Step: 4	Solder transistor
There is just one transistor to solder, Q1, BC337. / Ensure the flat side of the transistor aligns with the PCB markings.

Step: 5	Solder IC holders
		There are two 14pin IC holders and one 8 pin IC holder. These fit into the areas marked U1, U2 and U3. / Ensure correct orientation! / Ensure the notch on the holder aligns with the notch shown on the PCB.

Step: 6	Solder Switch and Potentiometer
The switch fits into the holes marked SW1. The switch knob goes off the PCB. / Solder all metal tabs. / The potentiometer fits into the holes marked RV1. There are 5 pins to align and the pins might need slightly moving to ensure they align correctly. / Solder all metal tabs.

Step: 7	Solder Speaker
		The speaker has a slightly unusual mounting method. / The speaker base fits through the large hole in the PCB and the speaker tabs alight with the PCB tabs. / Use an offcut of resistor lead and solder two small leads from the PCB (as shown). / Then pt the speaker in place and solder the small wires to the speaker. / This method holds the speaker in place, as well as being the electrical connection.

Step: 8	Solder PP3 battery connector
Nearly there! / The PP3 battery clip as two wires: one positive (red) and one negative (black). / I usually put a knot in the cable for strain relief. / The cables then go through the larger holes and are fed back into the solder pads. / The red cable goes through the hole to the pad marked “+”.

Step: 9	Insert ICs
		Now we need to insert the ICs into their holders. / Ensure the notches align with the notches on the IC holders and the PCB. / U1 is the LM386 (8 pin) / U2 is the TL074A (14 pin) / U3 is the 4024 (14 pin)

Step: 10	Insert battery and test
Add a PP3 9V battery to the battery clip. Switch the unit on. / You may hear a squeal from the device. Adjust potentiometer until you just do not hear any noise. / The red LED should also flash when the speaker clicks. / Use a reel of sticky tape to test. Slowly peel the tape off the reel and you should hear crackles from the speaker. This is picking up high frequency sound from the glue breaking. You can also test by pointing at a compact fluorescent light bulb. These switch at around 100kHz and hence give off ultrasonic noise.

Step: 16	PCB is finished!
		Have a nice cup of tea.

Enclosure Instructions:
Step: 1	Push out laser-cut parts and peel off protective layer
Sometimes not all the small laser-cut pieces have been removed. These can be pushed out using the point of a screwdriver. Only slight force should be required. / There is a protective film on one side of the laser cut parts. This can be removed by peeling off the film.

Step: 2	Screw down the PCB
		The PCB is held onto the back plate using the M3 10mm screws and the hex spacers. / The back plate has the text facing to the back. / The screws fit through the back plate then through a small circular spacer ring and then through the PCB. / It is then held in place using the threaded hex spacer. / Do this for all four corners of the PCB.

Step: 3	Add end spacers
To hold the end spacers in place we again use the 10mm screws and 2 of the hex spacers. / Put them through the back plate and slightly screw the hex spacer onto the screw. / Do not fully tighten this, as it will need to spin to be adjusted in the next step.

Step: 4	Add battery holders
		The battery holders are 6 spacers which holds one end of the battery, with the other end being held the notch in the PCB. / There are three types of spacer: / 1 x narrow 3mm spacer (in white frosted plastic) / 4 x wide 3mm spacers (with an “M” etched on them). / 1 x narrow 2mm spacer in clear plastic. / These fit onto the hex spacers we just added. / First add the narrow 3mm piece. / Then the 4 wide 3mm pieces (marked “M”). / Put the battery into the enclosure. The PP3 battery clip fits within the wider section, with the cable able to come out of the side. / The final narrow 2mm space is put on top.

Step: 5	Fit top cover
The front cover is then put on with the text facing upwards. / Use the final 6 x 6mm M3 machine screws to hold the front cover in place. / These fasten into the threaded hex spacers. / Note: Some covers do not have the hole for the LED. The LED can be seen through the frosted plastic, so it is not needed.

Step: 6	Finished!
		That is the unit finished! / The on/off switch and the potentiometer are accessible via the side of the unit. / You now have your own bat detector. / There are many things you can investigate including: / Nature: monitor bats, mice and rats / Electrical: Check the sound from switching power supplies and fluorescent lights

Please note: This unit is NOT waterproof. Do NOT leave outside if it will get wet.

Contact details:
We would like you to be happy with this kit. If you are not happy for any reason then please contact us and we will help to sort it out.

Please email hello@curiouselectric.co.uk with any questions or comments.
Please tweet us at @curiouselectric

If any parts are missing from your kit then please email hello@curiouselectric.co.uk with details and, if possible, where the kit was purchased.

More technical information can be found via www.curiouselectric.co.uk

This kit has been designed and produced by:
The Curious Electric Company
hello@curiouselectric.co.uk
www.curiouselectric.co.uk
Hopkinson, 21 Station Street, Nottingham, NG2 3AJ, UK

History

This kit is based upon a circuit originally published by Elektor Electronics:
 http://www.elektor.com/magazines/2011/november/simple-bat-detector.1971945.lynkx

and was originally developed as a workshop for Nottingham Hackspace: www.nottinghack.co.uk

Circuit Schematic

Resistor Colour Codes